| City of Houston Fire Marshal’s Office | In Home Daycare |
| --- | --- |
| Inspection Checklist and Notice of Violation |  |

| FPU: | Owner’s Name: |
| --- | --- |
| Phone: Address: Zip Code: Date: |
| Number of Children Enrolled: ______ Number of Children Present: _______ Number of Staff Members Present: ______ |
| ( Address - Post building address numbers – 4” numbers in height and visible from the street. | (Fire Extinguishers – provide approved extinguishers for each floor of this home (2A-10BC). There shall be no less than a 75 feet path of travel distance between extinguishers. |
| ( Evacuation Plan -Provide a fire safety evacuation Plan with evacuation route posted. | (Fire Drill - provide documentation of monthly fire drills to Fire Marshal |
| ( Posting of Floor Plans – a floor plan showing the proper evacuation routes shall be posted in each room and in other areas of the home normally occupied by children. | (Smoke Detectors - Provide smoke detectors for each sleeping rooms/areas, and for each story within the dwelling unit, and in the immediate vicinity of bed-rooms. |
| ( Door Locks – remove all unapproved locks and latching devices from all exit doors. | ( Exit Doors and Windows - Do not obstruct exit doors. Burglar bars shall be openable from the inside without the use of tool or special knowledge. |
| ( Door Locks - Door locks and latches shall be openable from the inside without the use of a key or tool. | (Utility Equipment - Provide accessibility to electrical breaker panel, electric and gas meters and cut-offs. |
| ( Extension Cords – extension cords and flexible cords shall not be a substitute for permanent wiring. | ( Electrical Shock Hazards – provide cover plates for wall switches, wall plugs and electrical panels. Exposed wiring shall be removed. Label all electrical circuits |
| ( Clearance from Combustibles - Provide 3 feet of clearance in all directions between combustible materials and room heaters and other heat producing devices. | ( Storage - discontinue storage of combustibles within 36 inches of a water heater. All storage shall be kept neat and orderly. |
| ( | ( |
| ( | ( |
| ( | ( |
| ( | ( |
| ( | ( |
| Important Note: This list is not all inclusive of the requirements for home daycares. It is only intended to be a guideline for some basic home daycare inspection requirements. ALL VIOLATIONS SHALL BE CORRECTED BY THE REINSPECTION DATE: _______________________ A $75.00 REINSPECTION FEE AND/OR CITATIONS MAY BE ACCESSED FOR ANY ADDITONAL REINSPECTIONS. FIRE INSPECTOR: ______________________________________ PHONE NUMBER______________________________________________ Person Receiving Report: Printed Name and Title: Date Inspection Completed: _____/_____/______ |