| ROOF / PENTHOUSE LEVEL |
| --- |
| Y | N | Items to check for: Code references: |
|  |  | Standpipe manifold valves at roof level; at upper standpipe terminus FC 901.6 |
|  |  | Standpipe pressure gauge at roof manifold or standpipe terminus FC 901 / FC 907.20.5 |
|  |  | All standpipe pressure gauges have double drain assembly F C 901.6 |
|  |  | Building Lightning rod ground wire connected to standpipe components FC 605.5.4 |
|  |  | Gravity tank(s) provided for standpipe water supply |
|  |  | Wooden cooling tower structure(s) ; Protected by Sprinklers or Fire Hoses |
|  |  | Building emergency generator(s) located on roof ; in a penthouse |
|  |  | Emergency generator has 2-hour occupancy separation FC 703.1 |
|  |  | Approved fuel storage tank / fuel storage containers for emergency generator(s) FC 3404 |
| Type of fuel for generator: | Diesel fuel or | Natural Gas |
|  |  | Approved Helistop on roof, with spill containment FC 1107.3 |
|  |  | Adequate fire protection provided for Helistop FC 1107.7 |
|  |  | Approved fire department access to roof FC 504.3 |
|  |  | Elevator penthouse / air handler equipment room located on roof |
|  |  | Fire extinguisher(s) and fire hose(s) in penthouse, properly mounted, identified and service tagged Service tags current: FC 906.2 |
|  |  | Stairway roof access through penthouse or mechanical room |
|  |  | Exit signs provided and properly maintained FC 1003.2.10.4 / FC 1010.3 |
|  |  | Exposed electrical wiring, missing electrical equipment covers, parts, etc. FC 605.1 |
| Electrical breaker panels: | Open slots – missing inserts or parts: FC 605.1 |  | Missing, faded panel index cards or directories, inadequate labeling: FC 605.3.1 |  |
|  |  | Stairwell pressurization present; smoke removal equipment present |
|  |  | Combustible storage in air handler, electrical or mechanical room(s) FC 315.2.3 |
|  |  | Floor penetrations properly sealed with approved 2-hr fire stop materials FC 703.1.1 |
| EXIT STAIRWAYS |
|  |  | Water pressure gauges, with double drain assembly, installed at standpipe upper terminus FC 901.6 |
|  |  | 2-hour fire rating maintained throughout enclosed exit stairway system FC 1003.3.3 |
|  |  | Emergency Lighting provided; Battery Units only FC 1003.2.11.2 |
|  |  | Free of storage & obstructions FC 804.2 / FC 1011.3 |
|  |  | Electronic egress &/or exit devices on stairway doors | Permitted & Approved: FC 1003.3.1.8.2 / FC 1003.3.1.3.4 |
|  |  | Required stair identification, terminus & roof access signs provided in stairway FC 1005.3.2.4 |
|  |  | Approved reentry means provided on all required reentry floors FC 1005.3.2.4 |
|  |  | Required stair identification and reentry signs provided on occupancy side of stairway doors FC 1005.3.2.4 |
|  |  | Exit stairways discharge to the exterior; Discharge back into building |
|  |  | Approved exit door devices on exit level discharge doors FC 1003.3.1.8 |
|  |  | Approved area of discharge; provided with emergency lighting provided throughout FC 1003.2.11.2 / FC 1010.5 |
|  |  | Standpipe hose valve thread protective caps in place and tight FC 901.6 |
|  |  | Pressure reducing valves / devices provided on stairway standpipe outlets |
| EXIT CORRIDORS |
|  |  | 1-HR corridor fire rating maintained on multi-tenant floors FC 1004.3.2 |
|  |  | 2-HR corridor fire rating maintained on Sky-Lobby floors FC 1004.3.2 |
|  |  | Exit signs provided and properly maintained FC 1003.2.10.4 / FC 1010.3 |
|  |  | Corridors free of storage and / or obstruction FC 804.2 / FC 1011.3 |
|  |  | Approved elevator lobby evacuation signs and graphics provided FC 404.5 |
|  |  | Electronic locks on corridor doors | Permitted & Approved FC 1003.3.1.3.4 |
|  |  | Electronic locks on elevator lobby doors | Permitted & Approved FC 1003.3.1.3.4 |
|  |  | All elevator lobbies have adequate and approved exiting FC 1003.3.1.8 |
|  |  | Approved emergency Exitway lighting provided FC 1003.2.11.2 / FC 1010.5 |
|  |  | Emergency Exit lighting via: Generator Battery units FC 1010.5 |
|  |  | Janitorial/storage closets/rooms approved storage heights maintained FC 315.2.1 |
|  |  | All Electrical and Mechanical rooms properly identified FC 605.1 |
|  |  | Electrical & mechanical rooms free of combustible storage FC 315.2.3 |
|  |  | Electrical service panels unobstructed, 30 inch clearance work space FC 605.3 |
|  |  | All electrical control boxes, throw switch boxes, breaker switch panels adequately identified and labeled FC 605.3.1 |
|  |  | Approved light guards / bulb protectors in place where required FC 605.10 |
| TENANT AREAS |
|  |  | Adequate, approved exiting provided and maintained: no exiting through storerooms, kitchens, mechanical rooms, or other hazardous areas FC 1011.1 / FC 1011.3 |
|  |  | Approved exit door locking devices provided FC 1003.3.1.8 |
|  |  | Electronic egress control devices provided (magnetic locking devices) FC 1003.3.1.8 |
|  |  | Electronic egress control devices permitted and approved FC 1003.3.1.3.4 |
|  |  | Exit signs maintained in proper working conditions FC 1003.2.10.4 / FC 1010.3 |
|  |  | Adequate exitway directional signs provided and properly positioned FC 1003.2.10.1 |
|  |  | Exit doors adequately identified and distinguishable from other doors FC 1003.3.1 |
|  |  | Exit pathways free from storage and obstruction FC 804.2 / FC 1011.3 |
|  |  | File / storage rooms / spaces maintained at approved storage heights FC 315.2.1 |
|  |  | Tenant fire extinguishers properly mounted, identified and service tagged FC 906.2 |
|  |  | Fire hose and fire extinguisher cabinets unobstructed F C 508.5.4 |
|  |  | Approved special fire suppression systems identified and maintained FC 901.6 |
|  |  | Electrical panels and equipment unobstructed FC 605.3 |
|  |  | Electrical wall outlet, switch cover plates, control boxes in place FC 605.1 |
|  |  | Electrical extension cords used in an approved manner FC 605.5 |
|  |  | Power taps (strips) used in an approved manner FC 605.4.1 |
|  |  | All compress gas cylinders properly secured or stored FC 3003.3.3 |
|  |  | All clothes dryers in use are properly vented FC 603.5 |
|  |  | Ceiling tiles in place, in all areas where installed or required to help prevent fire/ smoke extension and increase efficient of smoke detection and fire suppression systems FC 703.1 |
|  |  | All flammable and combustible liquids stored in approved manner FC 7902 |
|  |  | Flammable / Combustible Liquid - storage, use and handle permit required; Permit current FC 105.6 |
|  |  | All Propane usage in accordance with code requirement for size and storage FC 3803.2 |
|  |  | Approved Lead Acid Battery system(s) in use FC 608 |
|  |  | Lead Acid Battery system permit required; Permit current FC 601.2 |
|  |  | Hazardous materials in permitted quantities in use FC 2701 |
|  |  | Hazardous materials – storage, use and handling permit required; Permit current FC 2701.4 |
|  |  | Paint or spray finish room(s) present FC 1504 |
|  |  | Paint/spray finish room(s) maintain in accordance with Fire & Building Codes; Permitted ; Permit current FC 1501.2 |
|  |  | Approved trash & waste stored provided FC 304.2 |
|  |  | Dumpster permit required; Permit current FC 105 |
| COOKING & DINING FACILITIES |
|  |  | Assembly Permit required; Permit current FC 105 |
|  |  | Approved Certificate of Occupancy / Certificate of Compliance posted FC 102.3 |
|  |  | Gas pressure / leak test required; current (every 5 years) FC 603.9.2 |
|  |  | Kitchen provided with approved vent hood system (wherever grease laden vapors are produced) FC 609.2 |
|  |  | Kitchen vent hood provided with approved fire suppression system FC 904.2.1 |
|  |  | Vent hood fire suppression system inspected / tagged every 6 months FC 904.6.11.4 |
|  |  | Kitchen cooking surfaces, floors, walls and hood systems free of grease and oil accumulations FC 904.6.11.3 |
|  |  | Approved fire extinguisher(s) provided for kitchen and dining areas FC 904.11.5 / FC 906.4 |
|  |  | Approved storage height clearance maintained in all storage areas: Sprinklered - 18 inches Non-sprinklered - 24 inches FC 315.2.1 |
|  |  | No electrical shock hazards present in walk-in freezers / chillers (no exposed wiring or light bulbs) FC 605.1 |
|  |  | Approved exiting maintained in kitchen and dining areas FC 1004.3.1 |
|  |  | Proper use of power taps and extension cords observed FC 605.4 / FC 605.5 |
|  |  | All electrical breaker panels and control switches labelled; unobstructed FC 605.3.1 / FC 605.3 |
|  |  | Exit signs provided as required and properly maintained FC 1003.2.10.4 / FC 1010.4 |
|  |  | Approved trash and waste storage provided FC 315 |
| MAIN LOBBY / EXIT DISCHARGE LEVEL |
|  |  | Main building exit doors have proper signs provided, as needed FC 1003.3.1.8 |
|  |  | All electronic egress control devices approved and permitted FC 1003.3.1.8.2 / FC 1003.3.1.3.4 |
|  |  | Areas of exit discharge adequate and safely maintained FC 1011.3 |
|  |  | Approved Fire Command Center provided and maintained FC 509.1 |
|  |  | Fire Depository Box provided & maintained; Permit current FC 105 |
|  |  | Fire Alarm system in proper working order and inspection tagged FC 901.6 / FC 1007.1 |
|  |  | Elevator(s) in working order; Fire Service recall provided FC 607.1 |
| BASEMENT / BELOW GRADE / WINDOWLESS LEVELS |
|  |  | Stairway barriers in place between exit discharge level and basement FC 1005.3.2.3 |
|  |  | Basement / Windowless levels fully sprinkled FC 901.6 |
|  |  | Adequate unobstructed exiting provided throughout FC 804.2 / FC 1011.3 |
|  |  | Adequate Exit and Exit Directional signs provided and maintained FC 1003.2.10.4 |
|  |  | Approved emergency exit lighting provided FC 1003.2.10.5 / FC 1010.3 |
|  |  | All combustible storage kept at approved heights and aisle widths FC 1103.3.2.2 |
|  |  | Light guards / tube protectors provided as required FC 605..10 |
|  |  | Fire hoses and fire extinguishers provided, identified, unobstructed and service tagged; Service tags current FC 901.6 / FC 907.20.2 |
|  |  | No Class I flammable liquids in use or being stored in basement FC 3404.3.5.1 |
|  |  | All flammable and combustible liquids properly stored in approved rooms / cabinets FC 3404.3 |
|  |  | Trash and waste stored in approved location FC 304.1 |
|  |  | All electrical panels labeled and have directories FC 605.3.1 |
|  |  | All electrical control panels and switches accessible / unobstructed FC 605.3 |
| CENTRAL PLANT / MAINTENANCE/ SERVICE AREAS |
|  |  | Standpipe system(s) risers and valves adequately identified; inspected and service tagged; Service tags current FC 901.6 / FC 903.5 / FC 907.20.5 |
|  |  | Sprinkler system(s) risers and valves adequately identified; inspected and service tagged; Service tags current FC 901.6 / FC 903.5 / FC 907.20.5 |
|  |  | Fire pump(s) and water supply tank(s) inspected and tagged; Service tags current FC 901.6 / FC 903.5 / FC 907.20.5 |
|  |  | Boiler Permits current |
|  |  | Elevator permits current |
|  |  | All flammable and combustible liquids properly stored FC 3404 |
|  |  | All required Fire Department permits current FC 105 |
|  |  | All fire hoses and fire extinguishers properly mounted, identified, serviced and tagged; Service tags current FC 901.6 / FC 903.5 / FC 907.20.5 |
|  |  | All hazardous chemical identified and properly stored; FC 2701 Permit required & current FC 105 |
|  |  | Adequate Exit and exit directional signs provided FC 1003.2.10.1 |
|  |  | All compressed gas cylinders properly stored FC 3003.3.3 |
|  |  | Service and storage areas maintained clean and orderly, free of excess combustible waste and storage FC 304 |
|  |  | Fire alarm system(s) fully operational and tagged; Service tags current FC 901.6 / FC 903.5 / FC 907.20.5 |
|  |  | Any special fire suppression systems properly maintained and tagged FC 901.6 |
|  |  | Electrical panel and switch adequate labeled; unobstructed ; no missing or exposed parts or wiring FC 605.1 & FC 605.3 |
|  |  | Emergency generator(s) inspected and have current tag(s) FC 901.6 / FC 903.5 / FC 907.20.5 |
|  |  | Approved generator fuel storage provided; spill containment FC 3404 |
| PARKING FACILITIES |
|  |  | All Exit signs readily visible & in proper working order FC 1003.2.10 |
|  |  | Fire hoses provided and identified; current inspection and tags FC 901.6 |
|  |  | Adequate Fire extinguishers provided and identified; current tags FC 906 |
|  |  | Approved flammable and combustible liquid storage provided FC 3404 |
|  |  | Emergency exit lighting in proper order, where required FC 1003.2.10.1 |
|  |  | Standpipe system inspected and tagged FC 901.6 |
|  |  | Standpipe upper terminus provided with approved pressure gauge(s), with double drain valve assembly FC 901.6 |
| GENERAL BUILDING ITEMS |
|  |  | Approved Certificate of Occupancy / Certificate of Compliance posted FC 102.3 |
|  |  | All Fire Department Connections maintained, properly identified and unobstructed FC 901.6 / FC 903.5 / FC 907.20.5 |
|  |  | All storage area and maintenance spaces shall be orderly FC 315.2 |
|  |  | No fueled equipment stored in building FC 315.2.5 |
|  |  | All exterior exit doors have approved discharge landings FC 1003.13.1.4 |
|  |  | All exterior exit discharge pathways have adequate lighting to the public way FC 604.2.4 |
|  |  | Building’s address shall be plainly visible and legible from the street FC 503.3 |
|  |  | Approved Fire Lanes needed ; in place and maintained FC 503.1 |

This guide is not intended to be complete and totally comprehensive. Its intent is as a quick reference for the most commonly noted items to be aware of or observed during general high-rise building inspections.  All Fire Code reference numbers are taken from the City of Houston Fire Code (International Fire Code, 2000 ed., as amended).